## Slide 1: Keystone I Boot Procedure Introduction
China Multicore Application
Mar, 2014

## Slide 2: Agenda
Keystone I Boot Overview
Rom Boot Loader
Intermediate Boot Loader

## Slide 3: Keystone I DSP Family
C667x
Fixed/Float 32-bit DSP (up to 8 cores) up to 320 GMAC/160 GFLOP @ 1.25GHz
32KB L1P
32KB L1D
512KB L2 Per Core
4MB Shared L2
72-Bit DDR3-1333
Network Coprocessor
Multicore Navigator
SYS/BIOS, Multicore SDK
C667x
C665x
Fixed/Float 32-bit DSP (up to 8 cores) up to 320 GMAC/160 GFLOP @ 1.25GHz
32KB L1P
32KB L1D
1MB L2 Per Core
1MB Shared L2
32-Bit DDR3-1333
Multicore Navigator
Power Optimized
SYS/BIOS, Multicore SDK
C665x
C6670
Fixed/Float 32-bit DSP (4 cores) up to 160 GMAC/80 GFLOP @ 1.25GHz
32KB L1P
32KB L1D
1MB L2 Per Core
2MB Shared L2
72-Bit DDR3-1333
Network Coprocessor
Wireless Application Accelerators
Multicore Navigator
SYS/BIOS, Multicore SDK
C6670

## Slide 4: Reset Types
Reset Types | Initiator | Exception | Boot Pin | Boot Process
POR (Power On Reset) | POR active low RESETFULL active low | None(Reset everything on DSP) | Latched and update | Yes
Hard Reset | RESET active low Emulation PLLCTL register Watchdog timers | Test/emu logic Reset isolation modules | No | Yes
Soft Reset | RESET active low PLLCTL register (RSCTRL) Watchdog timers | Test/emu logic reset isolation modules EMIF16 MMRs, DDR3 EMIF MMRs, the sticky bits in PCIe MMRs | No | Yes
C66x CorePac local reset | Software (through LPSC MMR) Watchdog timers LRESET pin | Only Reset CorePac without destroying memory | No | No

## Slide 5: Different Boot Image Location
Storage
  NAND Flash
  NOR Flash
  EEPROM
  FTP
Host knows memory map of the boot device
  SRIO DIO
  I2C
  Hyperlink
  PCIE
Host do not knows memory map of the boot device
  SRIO Message
  EMAC
  UART

## Slide 6: RBL and IBL
Rom Boot Loader
  RBL is a code used directly for the device startup
  RBL code is burned in the DSP ROM (Non-modifiable)
  Base address for the RBL is 0x20B00000
  Supported boot mode is fixed
Intermediate Boot Loader
  IBL is a code used for second-stage boot after RBL
  IBL code is always burned in the I2C EEPROM and can be modified by customers
  Base address for the IBL is in L2 or SL2 memory.
  Supported boot mode is easy to extend.
Rom Boot Loader
Intermediate Boot Loader

## Slide 7: Agenda
Keystone I Boot Overview
Rom Boot Loader
Intermediate Boot Loader

## Slide 8: RBL Process
Boot Start
Hiber Enabled
Check Hibernation
Latch Boot Mode Pins
Boot Parameter Table Init
PLL Required?
POR Reset
Branch to PWRSTATCTL
Branch to boot function
PLL bypassed
Boot Mode Specific Process
Initialize the PLLs
YES
NO
NO
YES
YES
NO

## Slide 9: Boot Mode Pin
Boot mode and configurations are chosen using bootstrap pins on the device.
  Pins are latched and stored in13 bits of the DEVSTAT register during POR.
The configuration format for these 13 bits are shown in the table:
Boot Device [2:0] is dedicated for selecting the boot mode
Device Configuration [9:3] is used to specify the boot mode specific configurations.
PLL Multi [12:10] are used for PLL selection. In case of I2C/SPI boot mode, it is used for extended device configuration. (PLL is bypassed for these two boot modes)
Boot Mode Pins |  |  |  |  |  |  |  |  |  |  |  | 
12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
PLL Mult I2C/SPI Ext Dev Cfg |  |  | Device Configuration |  |  |  |  |  |  | Boot Device |  | 

## Slide 10: RBL Boot Modes
I2C Boot
  Master Boot (from I2C EEPROM)
  Master-Broadcast Boot(Master Boot followed by broadcast to slave cores)
  Passive Boot (external I2C host)
SPI Boot (from SPI flash)
SRIO Boot (from external host connected through SRIO, DIO or Message)
Ethernet Boot (boot from external host connected through Ethernet)
PCIe Boot (boot from external host connected through PCIe )
HyperLink Boot (boot from external host connected through HyperLink)
EMIF16 NOR Boot (boot from NOR Flash)
  Device Manual will detail supported types.
  C665x have NAND boot as well

## Slide 11: Boot Table
The image to be loaded into the device is converted to Boot Table recognizable by the RBL.
Code and data sections are inserted into the boot table automatically by the HEX conversion utility.
32-bit Program Entrance
32-bit Section Length
32-bit Section Address
Section Data…
32-bit Section Length
32-bit Section Address
Section Data…
……
0x00000000 (Boot Table End)

## Slide 12: Boot Configuration Table
A boot configuration table is used to program peripheral registers.
For example, DDR initilization…
Each table entry in the boot configuration table has three elements:
  The address to be modified
  The set mask
  The clear mask
Set Mask Bit | Clear Mask Bit | Operation
0 | 0 | Unchange
1 | 0 | Set
0 | 1 | Clear
1 | 1 | Toggle
Entry 0 | Address
 | Set Mask
 | Clear Mask
Entry 1 | Address
 | Set Mask
 | Clear Mask
… | …
Entry N Termination | 0x00000000
 | 0x00000000
 | 0x00000000
Notes: A boot configuration table is used if certain peripherals must be programmed with values that differ from their reset values before loading an application. For example, ifthe application needs to be loaded into DDR memory, the boot configuration table canbe used to program the DDR registers and enable the DDR peripheral before loading the application code into DDR.

## Slide 13: I2C Master
Uses 7 bits of device in Master Mode
Make the initial read of the I2C EEPROM while PLL is in bypass.
The initial boot parameter table will contain the desired clock multiplier which will be setup prior to any subsequent reads.
I2C Master Mode Device Configuration Field Descriptions |  | 
Bit Field | Value | Description
Mode | 0 | Master Mode
 | 1 | Passive Mode (bit field 9 is set to 1 and is used for this mode due to a bug in RBL)
Address | 0 | Boot From I2C EEPROM at I2C bus address 0x50
 | 1 | Boot From I2C EEPROM at I2C bus address 0x51
Speed | 0 | I2C data rate set to approximately 20 kHz
 | 1 | I2C fast mode. Data rate set to approximately 400 kHz (will not exceed)
Parameter Index | 0-31 | Identifies the index of the configuration table initially read from the I2C EEPROM
I2C Master Mode Device Configuration Bit Fields |  |  |  |  |  |  |  |  | 
12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3
Rsvd | Speed | Address | Rsvd | Mode (0) | Parameter Index |  |  |  | 

## Slide 14: I2C Passive
Uses 5 bits of device configuration
Does not drive the clock, but simply received on the specified address.
The I2C address is calculated by adding 0x19 to the I2C address specified in the device configuration.
I2C Passive Mode Device Configuration Field Descriptions |  | 
Bit Field | Value | Description
Mode | 0 | Master Mode
 | 1 | Passive Mode
Address | 0-7 | The I2C Bus address the device will listen to for data
I2C Passive Mode Device Configuration Bit Fields |  |  |  |  |  | 
9 | 8 | 7 | 6 | 5 | 4 | 3
Rsvd (Must be 1) | Mode (1) | Receive I2C Address |  |  | Reserved | 

## Slide 15: SPI
RBL reads either a boot parameter table or boot table from SPI flash
The table loaded can contain a boot parameter table for any other boot mode.
SPI Device Configuration Field Descriptions |  | 
Bit Field | Value | Description
Mode | 0 | Data is output on the rising edge of SPICLK. Input data is latched on the falling edge.
 | 1 | Data is output one half-cycle before the first rising edge of SPICLK and on subsequent falling edges. Input data is latched on the rising edge of SPICLK.
 | 2 | Data is output on the falling edge of SPICLK. Input data is latched on the rising edge.
 | 3 | Data is output one half-cycle before the first falling edge of SPICLK and on subsequent rising edges. Input data is latched on the falling edge of SPICLK.
4,5 pin | 0 | 4 pin mode used
 | 1 | 5 pin mode used
Addr Width | 0 | 16 bit address values are used
 | 1 | 24 bit address values are used
Chip Select | 0-3 | The chip select field value
Index | 0-3 | Specifies which parameter table is loaded
SPI Device Configuration Bit Fields |  |  |  |  |  |  |  |  | 
12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3
Mode (clk Pol/Phase) |  | 4,5pin | Addr Width | Chip select |  | Parameter Table |  |  | 

## Slide 16: EMIF16
Used to boot from the NOR flash.
RBL configures the EMIF16 , sets the boot complete bit and branches to EMIF16 CS2 data memory at 0x70000000.
No Memory is reserved by the boot loader.
Sleep / EMIF16 Configuration Bit Fields |  |  |  |  |  | 
9 | 8 | 7 | 6 | 5 | 4 | 3
Reserved |  | Wait Enable | Sub-Mode |  |  | 
Sleep / EMIF16 Configuration Bit Field Description |  | 
Bit Field | Value | Description
Sub-Mode | 0b00 | Sleep Boot
 | 0b01 | EMIF16 boot
 | 0b10 0b11 | Reserved
Wait Enable | 0b0 | Wait enable disabled (EMIF16 sub mode)
 | 0b1 | Wait enable enabled (EMIF16 sub mode)

## Slide 17: Ethernet
Ethernet(SGMII) boot configuration sets SERDES clock and device ID.
Ethernet (SGMII) Device Configuration Bit fields |  |  |  |  |  | 
9 | 8 | 7 | 6 | 5 | 4 | 3
SERDES Clock Mult |  | Ext connection |  | Dev ID |  | 
Bit field | Value | Description
Ext connection | 0 | Mac to Mac connection, master with auto negotiation
 | 1 | Mac to Mac connection, slave, and Mac to Phy
 | 2 | Mac to Mac, forced link
 | 3 | Mac to fiber connection
Device ID | 0-7 | This value is used in the device ID field of the Ethernet ready frame. Bits 1:0 are use for the SR ID.
SERDES Clock Mult The output frequency of the PLL must be 1.25 GBs. | 0 | x8 for input clock of 156.25 MHz
 | 1 | x5 for input clock of 250 MHz
 | 2 | x4 for input clock of 312.5 MHz
 | 3 | Reserved

## Slide 18: SRIO
SRIO boot configuration sets the Clock, Lane configuration, and mode
Rapid I/O Device Configuration Bit Fields |  |  |  |  |  | 
9 | 8 | 7 | 6 | 5 | 4 | 3
LaneSetup | Data Rate |  | Ref Clock |  |  | 
SRIO Configuration Bit Field Descriptions |  | 
Bit Field | Value | Description
Ref Clock | 0 | Reference Clock = 156.25 MHz
 | 1 | Reference Clock = 250 MHz
 | 2 | Reference Clock = 312.5 MHz
Data Rate | 0 | Data Rate = 1.25 GBs
 | 1 | Data Rate = 2.5 GBs
 | 2 | Data Rate = 3.125 GBs
 | 3 | Data Rate = 5.0 GBs
Lane Setup | 0 | Port Configured as 4 ports each 1 lane wide (4 -1x ports)
 | 1 | Port Configured as 2 ports 2 lanes wide (2 – 2x ports)

## Slide 19: PCI-E
In PCIe mode, most PCIE configuration registers should be setup by host remotely.
And then the host loads all the sections directly to the memory.
PCI Device Configuration Bit Fields |  |  |  |  |  | 
9 | 8 | 7 | 6 | 5 | 4 | 3
Rsvd | BAR Config |  |  |  | Reserved | 
PCI Device Configuration Bit Fields |  | 
Bit Field | Value | Description
SR ID | 0-3 | Smart Reflex ID
Bar Config | 0-0xf | See Next Slide

## Slide 20: Hyperlink
HyperLink boot mode boots the DSP through the ultra short range HyperLink.
The host loads the boot image directly through the link and then generates the interrupt to wake the DSP.
MCM Boot Device Configuration Field Descriptions |  | 
Bit Field | Value | Description
SR Index | 0-3 | Smart Reflex Index
Ref Clock | 0 | 156.25 MHz
 | 1 | 250 MHz
 | 2 | 312.5 MHz
Data Rate | 0 | 1.25 GBs
 | 1 | 3.125 GBs
 | 2 | 6.25 GBs
 | 3 | 12.5 GBs
MCM Boot Device Configuration |  |  |  |  |  | 
9 | 8 | 7 | 6 | 5 | 4 | 3
Reserved | Data Rate |  | Ref Clock |  |  | 

## Slide 21: Boot Multicore
During the boot process, the boot loader code is loaded into the L2 of corePac0 from the ROM.
The high 0xD23F (52K) bytes of L2 in all corePacs are reserved for the boot code. User should not overwrite this area.
All the other Cores will execute an IDLE.
User should load the image into the L2 of CorePacs they want to boot up.
Before setting the boot complete register, the user should also set the start address of the code in the respective BOOT MAGIC ADDRESS of the CorePac L2.
Finally, the user image should also write the IPC interrupt register to bring the required corePacs out of IDLE.

## Slide 22: Agenda
Keystone I Boot Overview
Rom Boot Loader
Intermediate Boot Loader

## Slide 23: Why IBL?
Boot from Nand flash on C667x/C6670
Boot from FTP server
Boot from images with different format
Boot from multiple images
Extended functions before boot
DSP上电
I2C启动
执行IBL
读取镜像
DSP启动

## Slide 24: IBL Support
Default device
Nand Flash
Nor Flash
TFTP
Image Format
ELF
BBLOB
Notes: BBLOB文件格式是16进制文件格式，在IBL中，BBLOB文件格式是从内存直接映射生成，现在也可以通过CCS直接生成BBLOB文件格式，通常BBLOB文件格式可用于启动Linux镜像。

## Slide 25: Easy to Use
Compile IBL source code in MCSDK directory
Burn IBL and parameter set to I2C EEPROM
Generate user image
Burn user image to Nand/Nor or upload to FTP server
Set boot mode pin on DSP
Power on DSP

## Slide 26: Reference
KeyStone Architecture Bootloader User Guide
TMS320C667x/0(C665x) Multicore Fixed and Floating-Point Digital Signal Processor Data Manual
BIOS-MCSDK User Guide
http://processors.wiki.ti.com/index.php/MAD_Utils_User_Guide
http://linux-c6x.org/wiki/index.php/IBL_version_1.0.0.11
www.deyisupport.com

## Slide 27: Backup